Report

Diagram/Pictures

As a case we used a modified guitar hero guitar (shown in figure 1). By modifying the stem and fitting a Raspberry pi into the base we were able to change it into a Simon Game. We have wired up the buttons and LED's using a main board that is located in the stem ( figure 2) and a jumper board located in the base on the guitar.

(Figure 1)	(Figure 2)

To make everything fit correctly we had to cut down the size of the buttons remove many of the screw connection points. We also had to slim the bread board down so that it would fit inside of the stem of the guitar.
(Figure 3)

GPIO 5
GPIO
16
GPIO 21
GPIO 19
GND
GPIO 12
Blue Button

Red Button

Yellow Button

Orange Button

Green Button

3.3V
GPIO 20
GPIO 22
GPIO 13
GPIO 6
GPIO 4

Green LED

Orange LED

Yellow LED

Red LED

Blue LED

R5
430 OHM
R4
430 OHM
R3
430 OHM
R2
430 OHM
R1
430 OHM

For this project we use GPIO pin's 5,12,16,19, and 21 for our buttons and GPIO pin's 4,6,13,20, and 22 for our LED's this can be seen in figure 3 above. Each LED's positive side is connect to the 3.3V power through a 430 OHM resistor and each negative side is connected to its designated GPIO pin. Where as the buttons are connected on one side to there set GPIO pin and the other side to the ground pin. Pins 19 and 20 run the blue LED button and LED, pins 21 and 22 run the red button and LED, pins 16 and 13 run the yellow button and LED, pins 12 and 6 run the orange button and LED, and pins 5 and 4 run the green button and LED.

Game modes:

Difficulties: